## Slide 1
ZVX146E Environmental Hydraulics
Lecture - 7
2024-2025 – WS

## Slide 2
Environmental Hydraulics - lectures:
November, 21 – lecture is cancelled
December, 5 – last lecture + questions
December, 12 – external lecturer
December, 19 – Final test

## Slide 3
Open Channel Flow

## Slide 4
TYPES OF FLOW
Based on temporal (Time, t) and spatial (Space,x)
Time Criteria
  Steady flow (dy/dt = 0). Water depth at one point same all the time. (Flow constant with time)
  Unsteady flow (dy/dt ≠ 0). Water depth changes all the time. (Flow variation with time)
Space criteria
  Uniform flow (dy/dx = 0). Water depth same along the whole length of flow.
  Non-uniform flow (dy/dx ≠ 0). Water depth changes either rapidly or gradually flow

## Slide 5
CLASSIFICATIONS OF OPEN CHANNEL FLOW
Open channel flow
Steady flow
Uniform
Varied
Unsteady flow
Varied
Uniform
Gradually varied flow
Rapidly varied flow
Gradually varied flow
Rapidly varied flow

## Slide 6
UNIFORM AND NON-UNIFORM FLOW
v1
v2
A1
A2
v1 = v2
A1 = A2
v2
v1
v1 ≠ v2
A1 ≠ A2
Uniform flow
Non-uniform flow
A1
A2
v1 > v2
A1 > A2

## Slide 7
STEADY FLOW IN OPEN CHANNEL – UNIFORM FLOW
Constant discharge -Q, other geometric and flow characteristics depended only on position
Uniform flow
y1 = y2; v1 = v2 S = SB = SE
v = const.
y1
Slope of bottom SB = S0 = const.
y2
2
1
EH
SE
SH
(v12/2g)
(v22/2g)
y
hf = Z = SE . L = SB . L
Z
L
hf
SB
Q = const. A = const. v = const.
L
EGL
PGL

## Slide 8
OPEN CHANNEL FLOW– STEADY FLOW - CHÉZY EQ.
Darcy-Weisbach eq. for open channel flow
velocity:
Chézy eq.
Uniform flow
SB = SPGL= SEGL
+ Continuity equation: Q = v . A

## Slide 9
Hydraulic characteristics
roughness coefficient - n
Chezy coefficient - C
velocity - v
discharge - Q
Geometric characteristics
depth - y
width of bottom - b
width of free water surface – B
wetted perimeter – P
area of cross-section – A
hydraulic radius – R = A/P
slope of bottom - SB

## Slide 10
Geometric characteristics
top width, B
is the width of the channel section at the free surface.
water area of cross-sec , A
is the cross-sectional area of the flow
normal to the direction of flow.
wetted perimeter, P
is the length of the line of intersection of
the channel wetted surface with a cross-sectional
plane normal to the direction of flow.
hydraulic radius, R = RH = A/P
is the ratio of the water area to its wetted perimeter.
depth, y or h
is the distance – bottom – free water level
hydraulic depth, yH = A/B (mean – average – depth)
is the ratio of the water area to the top width.
slope, m (1:m = tg a )
A
P
B
b
y(h)
1
m
a
yH

## Slide 11
TYPES OF CHANNELS (cross-sections):
Simple :
Compound:
Natural: irregular shape
is the channel for which the cross section is composed of several distinct subsections
2
3
1

## Slide 12
CHEZY EQUATION
Chezy coefficient
Manning (1889)
Pavlovskij (1925):
Bretting (1948):
Grain-size curve
- screen analysis (fine-grained)
- random sample (course-grained)
R >1 …
R <1 …

## Slide 13
Maximum canal side slopes
Sand, Soft Clay | 1: 3 (Vertical :Horizontal)
Sandy Clay, Silt Loam, Sandy Loam | 1:2
Fine Clay, Clay Loam | 1:1.5
Heavy Clay | 1:1
Stiff Clay with Concrete Lining | 0.5 to 1:1
Lined Canals | 1: 1.5

## Slide 14
Environmental Hydraulics

## Slide 15
n=0,026
n=0,038
n - roughness coefficient

## Slide 16
n=0,055
n=0,06
n=0,075
n - roughness coefficient

## Slide 17
n=0,130
n=0,051
n=0,063
n=0,079
n - roughness coefficient

## Slide 18
y
nB
nD
nB
OD
OB
OB
weighted average
- different roughness on wetted perimeter
→ equivalent roughness coefficient
A. Open channel flow - applications
navr=

## Slide 19
1. Calculation of discharge, Q
Given values: n, SB , y, m, b
Open channel – uniform flow - applications
Procedure:
1) evaluation of geometric parameters of cross-section
Trapezoidal profile
1 : m
y
b
n
n
n
2) Evaluation of Chézy coefficient
3) Discharge – Q – from Chezy and continuity eqs.
A
B
C
D
A

## Slide 20
1 : m
y
b
n
n
n
A
B
C
D
2) Evaluation of C –Chézy coefficient
3) Slope of bottom SB
Trapezoidal profile
2. Calculation of bottom slope - SB
Given values: n, Q , y, m, b
Procedure:
1) evaluation of geometric parameters of cross-section
A
Open channel – uniform flow - applications

## Slide 21
3a. Calculation of Manning roughness- n
Given values: Q , y, m, b, SB
1 : m
y
b
n
n
n
A
B
C
D
2) Chezy coefficient, C
3) Roughness coefficient -, n
Trapezoidal profile
Procedure:
1) evaluation of geometric parameters of cross-section
A
Open channel – uniform flow - applications

## Slide 22
3b. Calculation of Manning roughness- nB
Given values: nA , nC , Q , y, m, b, SB
1 : m
y
b
nA
nB
nC
A
B
C
D
Trapezoidal profile
Procedure:
1) evaluation of geometric parameters of cross-section
2) Chezy coefficient, C
3) Average roughness coefficient -, navr
4) Evaluation of roughness coefficient -, nB
nB
A
Open channel – uniform flow - applications

## Slide 23
4. Calculation of depth – y – by means of Rating curve
Given values: n, QG , m, b, SB
1 : m
y
b
n
n
n
A
B
C
D
Trapezoidal profile
Procedure:
Choice of depths - y1 , y2 , y3 …………………. yn.
1) evaluation of geometric parameters of cross-section
2) Chezy coefficient, C1..n
3) Evaluation of discharges Q1..n
Open channel – uniform flow - applications

## Slide 24
Rating curve (Q= f(y))
y
y
QG
Open channel – uniform flow - applications

## Slide 25
5. Calculation of bottom width, b
Given values: n, QG , y, m, SB
1 : m
y
b1..n
n
n
n
A
B
C
D
Trapezoidal profile
Procedure:
Choice of depths - b1 , b2 , b3 …………………. bn.
1) evaluation of geometric parameters of cross-sections
2) Chezy coefficient, C1..n
3) Evaluation of discharges Q1..n
Open channel – uniform flow - applications

## Slide 26
B. Compound channels
roughness coefficient, discharge Q = ΣQi
b
C ‘
y1
y2
F ‘
A
G
F
E
D
C
B
H
I
III
II
Q = QI + QII + QIII
PI
PII
PIII
AI
AII
AIII
nBC
nAB
nCD
nDE
nEF
….. Valid also for CC´ and FF´
Manning roughness:
Wetted perimeter:
AB + BC
CC´ + CD + DE + EF +FF´
FG + GH
nFG
nGH
Open channel – uniform flow - applications

## Slide 27
Open Channel Flow
Gradually varied flow

## Slide 28
GRADUALLY VARIED FLOW
The depth of flow can be changed by the conditions along the channel
Examples of Gradually Varied Flow are:
a) Backwater curve(dy/dl)  0 ................ (y1  y2 )
b) Downdrop curve (dy/dl)  0 ................ (y1  y2 )
c) Uniform flow (dy/dl)=0 ………………..…. (y1=y2 )

## Slide 29
Environmental Hydraulics
It is customary to compare the actual channel slope, sinθ or So with the critical slope Sc for the same Q.
There are five classes of channel slope giving rise to twelve distinct types of solution curves.
- So > Sc - Steep (S)
- So = Sc - Critical (C)
- So < Sc - Mild (M)
- So = 0 - Horizontal (H)
- So < 0 - Adverse (A)
Classifications of surface profile of gradually varied flow

## Slide 30
Environmental Hydraulics
So > Sc
Steep (S)
So < Sc - Mild (M)
So =Sc Critical(C)
So = 0
Horizontal (H)
So < 0
- Adverse (A)
Classifications of surface profile of gradually varied flow

## Slide 31
y1 ≠ y2; v1 ≠ v2
S ≠ S0 ≠ SE
(av12/2g)
y1
hf=SE .L
SB
y2
( av22/2g)
S B .L
Q = const. A ≠ const. v ≠ const.
SE
Steady flow in open channel – non -uniform flow
(Gradually varied flow)
L

## Slide 32
STEP BY STEP - method
Bernoulli equation (1) - (2)
(av12/2g)
y1
SE .L
SB
y2
(av22/2g)
S0 .L
1
2
L

## Slide 33
Slope of energy line SE
Continuity equation + Chezy equation
SE – slope of energy line (EGL)
Specific energy of cross-section
Distance between cross-sections (1) and (2) :

## Slide 34
Total L =  li
l1
l2
y1 = y POČ
y2
(1. step)
(2. step)
L
y
y3 = y KONC
yP
yP2
yP = (y1 + y2 )/2
DL = D EI /(i0 – iE)
( av22/2g)
2 types of examples
- L=? If we know yS and y3
- y = ? at a distance L

## Slide 35
„Step by step method“
y | SI | OI | RI | CP | K P | v I | avI2/2g | iE | EI | DEI | DLI | SDLI
y1 | C | C | C |  |  | C | C |  | C |  |  | 
yP |  |  | C | C | C |  |  | C |  | C | C | C
y2 | C | C | C |  |  | C | C |  | C |  |  | 
yP2 |  |  |  | C | C |  |  | C |  | C | C | C
y3 | C | C | C |  |  | C | C |  | C |  |  | 
( av22/2g)
DL = D EI /(i0 – iE)
iE = Q2 /CP .SP .RP 1/2
yP = (y1 + y2 )/2

## Slide 36
End